## Slide 1: An Arduino Workshop
A Microcontroller

## Slide 2: What is Arduino?
An open source platform (from Italy)
At its heart is a microcontroller, a computer on a chip
It is in effect a small computer
A microcontroller (sometimes abbreviated µC, uC or MCU) is a small computer on a single integrated circuit containing a processor core, memory, and programmable input/output peripherals.
The majority of microcontrollers in use today are embedded in other machinery, such as automobiles, telephones, appliances, and peripherals for computer systems
www.Arduino.cc – Free 140MB download

## Slide 3: Robotics at University

## Slide 4: Thingiverse.com

## Slide 6
USB Interface chip
Digital Connections
Microcontroller
(Atmega 328)
Reset Button
USB Port
Crystal
5V regulator
Power
(7-12V DC input)
Power Connectors
Analog Inputs
Serial Programming
Connector
Transmit (TX) Receive (RX)

## Slide 7: In more detail
Digital pins 3,5,6,9,10 & 11 can do pulse with modulation PWM (variable output) can be noted ~
‘add 14’
Arduino can do 16 million instructions per second (16MHz)

## Slide 8: How much do they cost?
$75 for a kit

## Slide 9: Where to start?
Come up with your own little project
Explore some crazy ideas
Look it up on the internet
Modify others’ blocks of code to your purposes
Then expand, get a kit, learn some more tools and try some more projects

## Slide 10: There is more than a few types….

## Slide 11: Before we start, handling the boards…
Once they are powered up please don’t touch the boards
Our fingers can create a short circuit on the board and ZAP it

## Slide 12: ‘Hello’ – of in our case Mr Blinky
We are going to plug our Arduino into the computer.
Then we create or load a sketch (program) and then upload it to the Arduino.
A lot of software programs use a hello command as a test when you first start.
The programming language we use with Arduino is called C
In our case we are going to do a blink test.

## Slide 13: Blink test
We need to tell the computer software what kind of Arduino we have:
<Tools>, <Board>, <Arduino UNO>
We need to tell the computer software where the Arduino is plugged in:
<Tools>, <Port>, <comx\Arduino> for Windows OS
<Tools>, <Serial Port>, <dev/ttyUSB0> for Linux OS
Then we load an example sketch:
<File>, <Examples>, <01.Basics>, <Blink>
The sketch (program) is now loaded into the window….
It make the LED blink (Light Emitting Diode)

## Slide 15: ‘ello, ‘ello, ‘ello, wot ‘ave we here….
*/ is a comments section
// are comments (the sign of good coding practice!)
Void setup is run once at the start to set up the environment
Void Loop is where the sketch program is mainly written and does all the work

## Slide 16: What does it all mean?
Arduino is a 5V system, if we plug in a 9V battery we fry things (up in smoke)
pinMode sets a particular pin to be either an input or an output
HIGH means ‘give all she's got Scotty’ = 5V
LOW means turn ‘off’ = 0V
Delay means to wait for ‘x’ milli seconds
digitalWrite is a name of something

## Slide 17: Programming Language (jargon)
pinMode is an Output in this example (rather than an input)
HIGH and LOW are arguments. They are passed to a function when it is called.
Delay is a singular argument. We can split arguments up with comma’s
digitalWrite is a name of a built-in function, it needs to know where to pass the information to when it is called. We put this in parentheses {} to define what is being called.
The parentheses and the code in between them are know as a block of code
We then compile our code and upload it to the Arduino

## Slide 18: Compile and Upload

## Slide 19: So lets mix it up
What might happen when you change the delay times?
Try it
Change the delay time and upload it to the Arduino
Observe what happens to the blink rates

## Slide 20: Just plug a LED onto the board….
Careful as we can cook the LED
Plug it into GND
And Pin 13
Wrong way around?

## Slide 21: IR Sensor
<File>, <Examples>, <01.Basics>, <AnalogReadSerial>
Black = ground
Red = power
Other (white) = A0
Our sensor uses near I/R (black & white)
Far I/R = heat sensor

## Slide 22: Serial Monitor
Open the serial monitor, the small magnifying glass in the top right hand corner
What do we see?
What happens when you move your hand towards the sensor?
Why does it stop if you put your hand on it and leave it there?

## Slide 23: Make the LED…..
<File>, <Examples>, <05.Control>, <IfStatementConditional>
What happens now?
The LED comes on as we trigger the sensor

## Slide 24: Time to get moving….
<File>, <Examples>, <Servo>, <Sweep>
180 servo, what does that mean?
Red/yellow = power
Black/brown = ground
‘other’ (orange) = comm’s
Which pin do we use for the orange connector?
Pin 9

## Slide 25: Move when I move….
<File>, <Examples>, <Servo>, <Knob>
The servo now changes drive direction based on you triggering the sensor

## Slide 26: The problem with servos….
They make bad wheels!
Replace the 180 servo with an unlimited servo

## Slide 27: Lets make some noise
Replace the LED with a speaker
<File>, <Examples>, <0.1Basic>, <Blink>
Why does it work?
How does it work? What are sound waves?

## Slide 28: Sounds good to me…
<File>, <Examples>, <02.Digital>, <toneMelody>
Read the sketch
Change the numbers and modify the tune

## Slide 29: Ta Da!
We have added sensors and had things respond to the world around them
We have modified code
We have repurposed code to what we want it to do
https://circuits.io/

## Slide 30: Crazy projects….
http://hacknmod.com/hack/top-40-arduino-projects-of-the-web/
https://www.instructables.com/id/Arduino-60/