## Slide 1: Networking
An introduction to working on the web

## Slide 2: Teacher notes
Aimed at Year 12-13
Not curriculum linked
Prior learning/knowledge: none
Learning objectives/outcomes:
Students understand that all devices have a unique physical address – MAC
This is linked to an IP address, that TCP/IP has a suite of tools (such as HTTP)
What is a gateway?
What does DNS do? Why?
Limits of TCP/IP v4, an awareness of NAT and DHCP, why LAN groups?
Why firewalls and software updates
Understanding some basic tools, such as ipconfig and ping
This is a large number of learning objectives, therefore consider this an introduction and thus not currently integrated into a proper lesson and plan

## Slide 3: Advanced organiser/resources
Computer access
Web access
Permissions to use command line tools
Whiteboard (to draw up network as you go)
Pad and paper for students to map out their own network

## Slide 4: Turn it on….
Electronic devices talk to each other
How do they know who to talk to? How to find them? What to say to get the answer they are seeking?
We use a combination of things:
A hardware address
An Internet Protocol address
We use a common language – TCP/IP

## Slide 5: What is a Computer Address?
Every electronic device that connects to a network has a unique identifier
The device uses a NIC (Network Interface Card)
Hard coded to your NIC is a unique identifier. This is your MAC address (Media Access Control), a 16 digit identifier
34-E6-D7-3D-33-CC (hexadecimal)
A MAC has an Organizationally Unique Identifier (QUI) well-known manufacturers at the star, some are:
Dell: 00-14-22 Nortel: 00-04-DC Cisco: 00-40-96 Belkin: 00-30-BD

## Slide 6: More on the MAC:
MAC is also called:
The Burned In Address (BIA)
Hardware Address
Physical Address

## Slide 7: TCP/IP
ARP (address resolution Protocol) translates between your MAC and you IP Address
What is your IP address?
Internet Protocol (IP)
Transmission Control Protocol (TCP)
IP just sends the message out, doesn’t care if you get it all (uses UDP)
TCP has a parity check to make sure you got all the information sent

## Slide 8: TCP/IP and MAC
So now our computer device has a link between its physical address and one for talking on a network.
Most devices uses TCP/IP today
There used to be a number of protocols in common use, not so much anymore (NETBEUI, WINS, NWLink, IPX/SPX, XNS…)

## Slide 9: Why TCP/IP?

## Slide 11: ARRRGGGHHH! Enough! Lets do….
Bring up the command line/DOS prompt (start, type in cmd, open)

## Slide 12: ipconfig /all

## Slide 13: If in Linux, sudo ifconfig

## Slide 14: DNS
Domain Name Server
Translates IP address’s into names and back again
E.g.
Servers can hold multiple web address for an IP address in DNS

## Slide 16: Next in the list
Physical MAC address
DHCP (more to follow) – this is where we got our IP address from
IPv6 (this follows on from DHCP/NAT and IPv4 – more to follow)
Our IPv4 IP address (192.168.10.x)
Subnet – helps define the IP address – a grouping
Lease – from DHCP
Gateway – where the computer should go to get to the outside world
DNS Servers
Legacy protocol support (WINS, NetBios)

## Slide 17: So what have we got so far?
Wherever working on any network start by drawing it up:
10.170.48.131
255.255.0.0
MAC: 60-57-18-94-4F-85
DHCP
1.1.1.1
DNS
10.100.32.32
DNS
10.100.32.30
WINS
10.100.32.42
WINS
10.100.32.41
Gateway
10.170.0.1

## Slide 18: Yours looks more like this:
DHCP, WINS, DNS
192.168.1.10
192.168.2.103
255.255.255.0
Gateway
192.168.1.1

## Slide 19: School network…
Teachers
Students
Gateway
192.168.1.1
Admin
BYOD
LAN 1
192.168.1.x
LAN 2
192.168.2.x
LAN 3
192.168.3.x
LAN 4
192.168.4.x

## Slide 20: DHCP
Dynamic Host Configuration Protocol
A pool of IP address's that can be assigned by DHCP server
Why?
With IPv4 we started to run out of IP address’s globally
So we use some reserved addresses as ‘internal’ ones
We use NAT (network Address Translation) to convert our ‘internal IP’ address to an ‘external one’ that can surf the web
We get our external IP address from our ISP (internet Service Provider)

## Slide 21: DHCP
Multiple pools
Subnets (masks)
Assign DNS, Gateway address’ automatically
Lease time
Home connection (DSL, VDSL, Cable) from ISP: DHCP
A company needs a fixed IP to host a web site: so pay the ISP for a fixed IP ($$$, and yes, being the internet there are ways around this)

## Slide 22: IpGoat.com

## Slide 23: Now where are we at with our Map?
10.170.48.131
255.255.0.0
MAC: 60-57-18-94-4F-85
DHCP
1.1.1.1
RELAY
DNS
10.100.32.32
vuwindrdns001
DNS
10.100.32.30
vuwincodns001
WINS
10.100.32.42
vuwindrdhcp001
WINS
10.100.32.41
vuwincodhcp001
Gateway 10.170.0.1
External IP:
130.195.253.19
ISP (VUW)
130.195.192.0/18
130.195.199.82
130.195.197.141
10.170.32.15
LAN: BYOD
130.195.199.196
SSID: Victoria
LAN:
Staff wireless
LAN: ecs.vuw.ac.nz
External IP:
130.195.199.185
HPLJ600 M602
130.195.6.247
Fuji-Xerox
Apeos Port IV 7080
130.195.7.240
Fuji-Xerox
Apeos Port IV 3375
130.195.7.241
LAN: BYOD
External IP:
130.195.253.23
Internal IP:
130.195.199.82
VUW
ECS
Gateway:
130.195.9.1
DHCP: 130.195.6.10
DNS: 130.195.6.10 SUBNET: 255.255.255.0
130.195.9.60
DNS: 130.195.5.12 WINS: 130.195.5.200 SUBNET: 255.255.255.0

## Slide 24: PING and Tracert
Two very handy tools
Ping 192.168.1.1
Ping www.name.com
Will show you a response from the targeted name/IP
tracert 192.168.1.1
tracert www.name.com
Tracert will show you the hops to the targeted name/IP
Tracert also does a DNS lookup for you - handy

## Slide 25: Add in Global DNS
DNS follows a hierarchy
Top level maintained by IANA
(Internet Assigned Numbers Authority)
Delegates down to people like Google
Google DNS: 8.8.8.8 and 8.8.4.4 (remember this)
ISP’s also have DNS
Configured automatically as part of DHCP for home connections
You can add other DNS servers from other ISP’s

## Slide 26: Security
Passwords
Anti virus
Software updates/Patches
Firewall
IPS – intrusion prevention/detection

## Slide 27: Add in a firewall
What is a firewall?
It controls traffic into and out of an organisation
It allows a LAN, server or group to communicate with another LAN, Server or group on SPECIFIC protocols
The last rule is always the clean-up rule (drop it if it doesn’t match any rule)

## Slide 28: How to hack…
Ping test – are you there?
This is called sniffing
Port scans (what is a port?)
Do you have port 110 open? Yes 110 = POP3 (Post Office Protocol) which is used by email servers, 80 = HTTP, etc..
Vulnerability testing
Password crackers (brute force)
The biggest threat is still physical access – I can then take all the time I want to crack your system
Reconnaissance, Initial Exploitation, Establish Persistence, Install Tools, Move Laterally, Collect Exfil, and Exploit

## Slide 29: How often do you get scanned?
Home user – every 15 minutes
Business - at least once every 5 minutes
Big corporate – every minute

## Slide 30: How to stop hackers
Make sure you AV is up-to-date
Make sure your software is patched up-to-date
Have a firewall
Good passwords (more than 8 characters, alpha-numeric)
Don’t give out your passwords EVER
Don’t open stupid links (hover over HTML links and it will tell you the destination, often fake…)
Nigeria isn’t your friend and they don’t have millions to transfer – i.e. if it is too good to be true then it is rubbish…

## Slide 31: Other security issues
So I cracked into your system what can/will I do?
Not so much delete your files, that’s destructive and childish….
Key logger to get CC details, passwords, etc.
Steal information (financials, pay details..)
Control essential services
Zombies (DOS attacks)
This is big business
Banking and financial sector
Big Global demand for staff, good at maths?

## Slide 32: I am not kidding
Vodafone built backdoor access into Greece's cell phone network for the Greek government; it was used against the Greek government in 2004-2005
Google kept a database of backdoor accesses provided to the U.S. government under CALEA; the Chinese breached that database in 2009.
https://www.schneier.com/
http://www.theregister.co.uk/
France rejects backdoors in encryption products. And for the right reasons, too. http://www.theregister.co.uk/2016/01/15/france_backdoor_law/
France joins the Netherlands on this issue. https://www.schneier.com/blog/archives/2016/01/michael_hayden_.html
Apple's Tim Cook is going after the Obama administration on the issue. https://theintercept.com/2016/01/12/apples-tim-cook-lashes-out-at-white-house-officials-for-being-wishy-washy-on-encryption/
Fitbit – picking up on when you are pregnant, or breaking up with a partner….
Geolocation data – ISIS drone strike

## Slide 33: Future considerations
Electronic voting
Control of military drones
Hijacking of cars and houses
Manipulation of data flow (traffic, stock markets…)
Skimming
Changing personal data

## Slide 34: Note
I have gone over the basics of networking
I have covered the basics of hacking
I have not covered how not to get caught
Do not try this, there is a number of fish hooks, such as where you get tools will most likely infect your device
It is fundamentally unethical and often illegal – so don’t do it

## Slide 35: Homework
http://www.imdb.com/title/tt2084953/
http://www.imdb.com/title/tt2177843/?ref_=tt_rec_tti

## Slide 36: Title and Content Layout with Chart
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 4.3 | 2.5 | 3.5 | 4.5
Series 2 | 2.4 | 4.4 | 1.8 | 2.8
Series 3 | 2 | 2 | 3 | 5

## Slide 37: Two Content Layout with Table
 | Group 1 | Group 2
Class 1 | 82 | 95
Class 2 | 76 | 88
Class 3 | 84 | 90
First bullet point here
Second bullet point here
Third bullet point here

## Slide 38: Title and Content Layout with SmartArt
Step 1 Title
Task description
Task description
Step 2 Title
Task description
Step 3 Title
Task description
Task description
Task description