## Slide 1: Raspberry Pi
A microcontroller
Raspberry Pi 2 Model B V1.1
RPi

## Slide 2: Computer in your hand
A microcontroller (sometimes abbreviated µC, uC or MCU) is a small computer on a single integrated circuit containing a processor core, memory, and programmable input/output peripherals. The majority of microcontrollers in use today are embedded in other machinery, such as automobiles, telephones, appliances, and peripherals for computer system.
A system on a chip (SoC) combines the required electronic circuits of various computer components onto a single, integrated chip (IC).
The difference between a SoC and a microcontroller often times is defined by the amount of random access memory (RAM).
A SoC is capable of running its own operating system.
Sooner or later you just need more power! (Arduino vs RPi)

## Slide 3: What can I do with rpi?

## Slide 4
Power - Micro USB 5v
DSI Display Connector
40 GPIO (Input /Output)
4 USB ports
10/100 T Base Ethernet port
4 Pole 3.5mm jack
(stereo audio & composite video)
HDMI Digital video out
SOC – System On a Chip
(Broadcom BCM2836) + 1GB RAM
SD Card (underneath)
CSI Camera Connector
Mounting hole
Close RUN header to reset Pi
SMSC LAN9514 USB Ethernet controller
Switching regulator for less power consumption
Power & activity LED’s

## Slide 5: Older Pi models

## Slide 6
85mm x 56mm

## Slide 7: Power
Can be powered by 4 AA batteries
We recommend rechargeable batteries
They produce less voltage and better meet the power feed requirements of the RPi

## Slide 8: Starting it up
Insert prepared SD card (already done) with OS installed
Connect HDMI to monitor
Connect RCA if HDMI not available
Connect a USB keyboard and mouse
Connect to a network (Ethernet or wireless USB)

## Slide 9: login
Standard user = pi
Standard password = raspberry

## Slide 10: Connecting to the RPi

## Slide 11: Enable ssh
Enter sudo raspi-config in the terminal
Then navigate to ssh
Hit Enter and select Enable or disable ssh server.

## Slide 12: Where’s my pi?
Find out the IP address of your Raspberry. In case you have access to the console you can also type the following command:
sudo ifconfig
Fing

## Slide 13: So what are we looking at?
The Desktop environment
The Shell
Kernel
Applications

## Slide 14: The Shell, or Bash:
Born Again SHell
Logged in as user ‘pi’
Logged into this host
Home directory (~)
Ordinary user
LXTerminal

## Slide 15: Directory Tree
/
bin
boot
dev
etc
home
lib
Lost+found
media
mnt
opt
proc
root
run
sbin
selinux
sys
srv
temp
usr
var
Bin – binaries – small programs that behave like commands in the shell
Boot – Linux kernel – heart of the OS
Dev – devices – a list of devices
Etc – various configuration files for all users
Home – directory for each user
Lib – libraries – used by different programs
Lost+found – corrupted files
Media – for managing removable storage devices
mnt – for managing removable storage devices that you mount
opt – optional software
proc – processes used by the Linux kernal
root – root user directory (top level admin)
Run – programs store data here for ready recall
sbin – software reserved for the root user
Selinux – security enhanced Linux
srv – sometimes used for storing data (like for FTP)
sys – used for Linux OS files
temp – temporary files
usr – for standard users for programs and files
var – files that vary in size (like DB and logs)

## Slide 16: Moving around in the directory structure
Absolute and relative paths
cd (change directory)
Relative path is like giving directions (refers to a subdirectory)
An absolute path is like giving a street address
cd [option] [directory]
cd /home/pi (absolute path, relative to root)
cd ~ (home directory, relative to home location)
cd ../../boot
cd.. (close directory)
cd – (go to previous directory)

## Slide 17: Command lines
Command –options argument (pi@raspberrypi ~ ls –X ~/python_games)
ls – to list directories and files
Remember this one:
ls –lh (list, long, human)

## Slide 18: Command lines for ls
-1 = results in a single column instead of a row
-a = display all (including hidden)
-F = put a symbol beside the filename to indicate file type
-h = long format (human readable)
-l = long format
-m = list separated by comma’s
-R = recursive (show directories and contents as well)
-r = display in reverse alphabetical order
-S = sort results by size
-t = sort by date and time last modified
-X = sort by file extension

## Slide 19: Moving around
CTRL + C (end task)
Autocomplete with the [TAB] key
↑↓ to cycle through previous commands you have entered
Turn screen output into a file using the > symbol (use >> to add something to an existing file)
Echo (displays whatever you write after it on screen, use $ to solve maths equations), date, cal

## Slide 20: Exercise
echo I made this file on > testfile.txt
date >> testfile.txt
cal >> textfile.txt
echo $((8+30+31+30+17)) Days until my Birthday! >> testfile.txt
Less testfile.txt
Note: keep names simple (capitals, hyphens, symbols can all have meanings)

## Slide 21: More commands
Mkdir (make directory, can do multiple –p option to make a folder in a folder, -v for verbose)
Rm (remove directory, -i for interactive = Y/N for each file, -R for recursive, -f for force)
*.txt or testfi*= wildcard
[] to match characters (e.g. [abc]*, [^abc]*, [a-c]*, photo[4-9].jpg)
cp (copy paste)
mv (move, also = rename)
Cat (list the content of files)
wc (word count) – gives # of lines, # of words, # of characters

## Slide 22: Is your software up-to-date?
Sudo = Super User DO
Root can be considered a security risk/hole
Package manager is called apt in the shell
sudo apt-get update
sudo apt-cache search games | less
sudo apt-get install name
Help can be found in many places… try type, help, man (manual), apropos, whatis, info
https://wiki.debian.org/ShellCommands
https://www.raspberrypi.org/documentation/usage/terminal/

## Slide 23: Trolled….
Watch out for:
rm –Rf /*

## Slide 25: Title and Content Layout with Chart
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 4.3 | 2.5 | 3.5 | 4.5
Series 2 | 2.4 | 4.4 | 1.8 | 2.8
Series 3 | 2 | 2 | 3 | 5

## Slide 26: Two Content Layout with Table
First bullet point here
Second bullet point here
Third bullet point here
 | Group A | Group B
Class 1 | 82 | 85
Class 2 | 76 | 88
Class 3 | 84 | 90

## Slide 27: Two Content Layout with SmartArt
Group A
Task 1
Task 2
Group B
Task 1
Task 2
Group C
Task 1
First bullet point here
Second bullet point here
Third bullet point here